## Slide 1
Customer-Facing Developments of
the Smart Grid
Ahmad Faruqui, Philip Q Hanser, and Sanem Sergici
Electric Grid Modernization Workshop
Massachusetts Department of Public Utilities
Boston, Massachusetts
November 14, 2012
The views expressed in this presentation are strictly those of the authors and do not necessarily state or reflect the views of The Brattle Group, Inc.

## Slide 2: The Smart Grid Opens Up a Number of Opportunities Involving the Customer
The most important activity is the rollout of Advanced Metering Infrastructure (AMI) .
  This features “Smart” Meters which record and digitally communicate electricity consumption data on frequent intervals (e.g., 15 minutes or hourly).
AMI acts as a gateway to offering dynamic pricing and time-of-use rates which can foster more responsive customer demand, improve load factors and lower average cost for all customers.

## Slide 3: What is Dynamic Pricing?
Simply put, it is “cost-reflective pricing”
Many ‘flavors’ exist
  Time variant rates (or time-of-use rates, TOU)
  Critical-peak pricing (CPP)
  Peak-time rebates (PTR)
  Variable-peak pricing (VPP)
  Real-time pricing (RTP)
  These can be combined to yield hybrid forms of dynamic pricing.

## Slide 4: Six Common Myths About Dynamic Pricing
Customers have never heard of it.
  But they encounter it almost every day in their other lives.
Electricity is a necessity and consumers won’t respond.
  The Arc of Price Responsiveness shows that they do respond.
Our prices are too low.
  But customers will be happier if they were even lower
Our prices are too high.
  Customers would be happier if they were lower.
It will harm low income consumers.
  Most low income consumers will see lower bills with dynamic pricing.

## Slide 5: Dynamic Pricing Enables Customer Choice Among Competing Pricing Products
Flat Rate
RTP
CPP
VPP
Inclining Block Rate
Seasonal Rate
TOU
Less Risk, Lower Reward
More Risk, Higher Reward
Super Peak TOU
PTR
Potential Reward (Discount from Flat Rate)
Increasing Reward

## Slide 6: Flat-Rate Pricing is Expensive
Flat Rates are inefficient.
  They do not signal to consumers when electricity is expensive to consume.
  In the US customers may be overpaying for electricity by about $7 billion/year.
    We take the FERC Staff estimate of 92 GW saved under universal dynamic pricing and value demand response at $75/kW-year.
Flat Rates are unfair.
  Under flat rate pricing, inter-customer subsidies may amount to $3 billion/year in the US.
    We scale up the results from a California rate design study that was sponsored by the Demand Response Research Center.

## Slide 7: Dynamic Pricing With or Without Enabling Technology Can Lead to Major Peak Reductions
The Arc of Price Responsiveness

## Slide 8: An Illustrative Case Study of Massachusetts
  The case study envisions that that AMI is rolled out in the state along with a representative portfolio of programs
    Assumptions are made about AMI deployment rates, likely customer participation rates, likely impact on peak demand and energy consumption per customer
    Aggregate impacts are then estimated as the product of the two preceding assumptions
    Benefits are estimated by estimating avoided costs created by changes in load shapes.
  The results from the case study are intended to be prospective and not prescriptive in any way
  Brattle prepared these results on its own initiative and is open to exploring the assumptions in greater depth during the Working Group process

## Slide 9: We quantify the net benefits using our iGrid model
  The iGrid model measures three main categories of net benefits enabled by AMI
    Demand response (DR)
    Energy efficiency (EE)
    Plug-in electric vehicles (PEV)
  In each category, we quantify the net benefits arising from avoided capacity costs, avoided energy costs, avoided carbon costs, and avoided gasoline costs
  iGrid was used recently to quantify the net societal benefits of AMI in Ameren’s service area in Illinois and has been used for assessing net benefits in other states such as Colorado

## Slide 10: Societal Costs of the Twenty-year AMI Rollout are Estimated per Customer
(1) The cost of installation is included in these price estimates.
(2) We assume a PEV cost premium of $9,500 in 2012.
(3) AMI cost is net of operational savings; this cost is assumed to be a one-time cost for all customers
(4) In the first ten years of the forecast, nominal technology costs (apart from AMI) decrease at a rate of 16% per year. In the next ten years, the costs decrease at a rate of 8% per year.
(5) Display is in-home display, PCT is programmable communicating thermostat, DLC is direct load control and HEMS is home energy management system
Per-customer Technology Costs in 2012
(Residential & Small C&I)

## Slide 11: Our Illustrative Scenario Assumes Full AMI Deployment and Opt-Out Dynamic Pricing in Massachusetts
  100% AMI deployment reached over 15 years
  PTR is assumed to be offered on an opt-out basis, reaching nearly 70% enrollment by 2032
  Some customers who opt out of the PTR enroll in a variety of other pricing and non-pricing programs (17% choose not to enroll in any DR option)
  A portion of participants in pricing programs are assumed to be equipped with “enabling technologies”
  Similar assumptions are used for C&I customers
  The AMI rollout is also assumed to encourage an incremental increase in PEV adoption
Residential Participation by Program
Key Assumptions (Illustrative)

## Slide 12: A Full AMI Rollout with Opt-Out Dynamic Pricing Can Potentially Yield Over $1.2 Billion in Net Societal Benefits
Net Present Value of AMI Deployment over 20 years

## Slide 13: Developments in Other States
Arizona
  Over two decades, Arizona Public Service has enrolled 51% of its customers on a voluntary TOU rate and the Salt River Project has enrolled about 30% of its customers on a voluntary TOU rate.
  In both cases, the TOU rate appeals to large consumers who avoid the upper tier of an inclining block rate by going with TOU.
California
  PG&E has enrolled 80,000 customers on CPP.
  SDG&E is offering PTR on an opt-out basis to 2 million customers.
  SCE is offering PTR on an opt-in basis and more than 2 million customers have signed on.

## Slide 14: US Developments (continued)
Illinois
  Both the investor-owned utilities, ComEd and Ameren, have enrolled about 25,000 customers on RTP in Illinois.
  A new state law calls for opt-in PTR to be offered statewide.
Mid-Atlantic Region
  BGE and PHI will be offering PTR to 2 million customers over the next few years in Delaware, Maryland and the District of Columbia.
  PJM is allowing price-responsive demand to be bid into its multi-state markets, as AMI and dynamic pricing are rolled out in its footprint of 51 million customers.
Oklahoma
  OG&E has begun rolling out VPP and hopes to sign up 20% of its customers over the next 3 years.
  By so doing, it hopes to avoid building a medium-sized power plant.

## Slide 15: International Developments
Australia
  The Federal Government recently announced its support for a national rollout of smart meters in order to lower power bills.
  The federal energy minister supports dynamic pricing.
  A three-tier solution is being proposed by the Australia Energy Market Commission for dynamic pricing applied to transmission and distribution rates.
    Mandatory for customers that use twice as much as the average residential customer
    Opt-in for low income and other vulnerable customers
    Opt-out for everyone else

## Slide 16: International Developments (continued)
Canada (Ontario)
  3.9 million (81%) residential and small business customers are on TOU rates under a regulated retail pricing plan (March 2012).
  All customers have the option of switching over to retail providers.
China
  Beijing: 62% of the population was on TOU rates by the end of 2003
  Hebei: 40,000 customers (about half of all sales) are on TOU rates Additionally, Hebei has instituted a mild CPP rate.
  Jiangsu: Voluntary residential TOU since 2003
  Shanghai: TOU rate with a 4.5-to-1 peak to off-peak price ratio
France
  Électricité de France has offered residential customers CPP across France through the tempo tariff since 1996.
  Roughly 400,000 customers have enrolled in the rate.

## Slide 17: International Developments (continued)
  Great Britain
  Consumer Focus found ~75% of consumers on TOU tariff are satisfied
  Most popular TOU tariff is the Economy 7 tariff, where consumers are charged a lower price for seven consecutive hours overnight.
  Ireland
  The Commission for Energy Regulation is currently assessing the pros and cons of mandating TOU tariffs and intends to publish its findings by the end of this year.
  Stakeholder engagement will follow in 2013.
Italy
  Currently, 28.8 million customers are on a TOU program.
    18.8 million are Residential Customers
    ~91% of these residential customers have defaulted to TOU tariff

## Slide 18: Pathways to the Future
Opt-in
  Makes sense but only if the dynamic pricing rate is net of the hedging premium in flat rates and if dynamic pricing rates are simple and easy for customers to understand
    The rates should offer customers significant savings potential and also be offered in a way that appeals to other customer needs besides just saving money.
Opt-out
  Best to offer it full bill protection for the first year and to phase this out over the next two to three years
    An alternative is to offer two-part rates
    Another alternative is to offer peak-time rebates

## Slide 19
Appendix

## Slide 20: A Glossary of Dynamic Pricing

## Slide 21: Dynamic Pricing Means Lower Rates for Thousands of Hours a Year and Higher Prices During a Few Hundred

## Slide 22: References
  Faruqui, Ahmad, Ryan Hledik and Jennifer Palmer, Time-Varying and Dynamic Rate Design, Regulatory Assistance Project, July 2012. http://www.raponline.org/topic/global-power-best-practice-series
  Faruqui, Ahmad and Doug Mitarotonda, “Energy Efficiency and Demand Response in 2020: A Survey of Expert Opinion,” The Brattle Group, November 2011. http://www.brattle.com/_documents/UploadLibrary/Upload990.pdf
  Faruqui, Ahmad and Eric Shultz, “Demand Growth and the New Normal,” Public Utilities Fortnightly, December 2012, forthcoming.
  Faruqui, Ahmad and Sanem Sergici, "Dynamic Pricing of Electricity in the Mid-Atlantic Region: Econometric Results from the Baltimore Gas and Electric Company Experiment," Journal of Regulatory Economics, August 2011.
  Faruqui, Ahmad and Sanem Sergici, "Household Response to Dynamic Pricing of Electricity – A Survey of 15 Experiments,“ Journal of Regulatory Economics, October 2010.
  Faruqui, Ahmad and Jenny Palmer, “The Discovery of Price Responsiveness – A Survey of Experiments Involving Dynamic Pricing of Electricity,” EDI Quarterly, April 2012. http://papers.ssrn.com/sol3/papers.cfm?abstract_id=2020587
  Faruqui, Ahmad and Jenny Palmer, “Dynamic Pricing and its Discontents,” Regulation, Fall 2011. http://www.cato.org/pubs/regulation/regv34n3/regv34n3-5.pdf

## Slide 23: References (continued)
  Faruqui, Ahmad and Neil Lessem, Managing the Costs and Benefits of Dynamic Pricing, Australian Energy Market Commission: Power of Choice Review, September 2012. http://www.aemc.gov.au/market-reviews/open/power-of-choice-update-page.html
  Faruqui, Ahmad. Illinois Commerce Commission, Docket No. 12-0244. Direct Testimony on Rehearing of Dr. Ahmad Faruqui, June 28, 2012.
  Faruqui, Ahmad. Illinois Commerce Commission, Docket No. 12-0244. Rebuttal Testimony on Rehearing of Dr. Ahmad Faruqui, September 11, 2012.
  Federal Energy Regulatory Commission staff. A National Assessment of Demand Response Potential. June 2009. http://www.ferc.gov/legal/staff-reports/06-09-demand-response.pdf
  Hanser, Philip Q, “Rate Design by Objective,” Public Utilities Fortnightly, September 2012.
  “Most British consumers satisfied with time of use tariffs,” METERING.COM. http://www.metering.com/node/21810 (accessed November 12, 2012).
  “Smart meter mandate coming for Australia?” SmartGridNews.com. http://www.smartgridnews.com/artman/publish/Technologies_Metering/Smart-meter-mandate-coming-for-Australia-5271.html#.UKG-KIfXYto (accessed November 12, 2012).
  Wood, Lisa and Ahmad Faruqui, “Dynamic Pricing and Low-Income Customers: Correcting misconceptions about load-management programs,” Public Utilities Fortnightly, November 2010, pp. 60-64. http://www.fortnightly.com/archive/puf_archive_1110.cfm

## Slide 24: Speaker Bio and Contact Information
Ahmad Faruqui, Ph.D.
Principal
San Francisco, California
Ahmad.Faruqui@brattle.com
925.408.0149
Dr. Faruqui has advised more than two dozen clients on demand forecasting issues, including utilities and transmission system operators in the United States and around the globe.
He has consulted with more than 50 utilities and transmission system operators around the globe and testified or appeared before a dozen state and provincial commissions and legislative bodies in the United States and Canada.
In addition, he has developed models for forecasting monthly and hourly loads for clients using a variety of econometric and time series methods. He helped develop an hourly load forecasting model to assist a competitive wholesaler in bidding for default service. For a utility, he diagnosed why energy sales were below forecasts even after adjusting for the effects of the economy. He assisted a transmission system operator understand why peak demand was being under-forecast by a large amount. And he assisted a regulated provider of steam analyze the customer’s decision to switch from purchasing steam to self-generating of steam and also to analyze the response of steam usage to rising steam prices. The analysis was carried out on a customer-by-customer basis and involved the use of discrete choice methods and conventional regression analysis.
More recently, Dr. Faruqui has been involved in the estimation of hourly, daily and monthly demand models in the context of dynamic pricing pilots. Dr. Faruqui has managed the design and evaluation of large-scale dynamic pricing experiments in California, Connecticut, Florida, Illinois, Maryland and Michigan. This work involved the estimation of a variety of econometric models for estimating customer response to prices that varied by time of day.
His work has been cited in publications such as The Economist, The New York Times, and USA Today and he has appeared on Fox News and National Public Radio. The author, co-author or editor of four books and more than 150 articles, papers and reports on efficient energy use, he holds a Ph.D. in economics and an M.A. in agricultural economics from The University of California at Davis, where he was a Regents Fellow.
The views expressed in this presentation are strictly those of the presenter(s) and do not necessarily state or reflect the views of The Brattle Group, Inc.
Insert corporate headshot here.

## Slide 25: Speaker Bio and Contact Information
The views expressed in this presentation are strictly those of the presenter(s) and do not necessarily state or reflect the views of The Brattle Group, Inc.
Speaker Bio and Contact Information
Philip Q Hanser
Principal
Cambridge, MA
Phil.Hanser@brattle.com
Phone: (617) 864-7900
Fax: (617) 864-1576
Mr. Hanser assists clients in issues ranging from utility industry structure and market power and associated regulatory questions, to specific operational and strategic issues, such as transmission pricing, generation planning, and tariff strategies. He also has expertise in fuels procurement, environmental issues, forecasting, marketing and demand-side management, and other complex management and financial matters.
Over his thirty years in the industry, Mr. Hanser has appeared as an expert witness before the Federal Energy Regulatory Commission (FERC), many U.S. and Canadian public utility and siting commissions, before arbitration panels, and in federal and state courts. He served six years on the American Statistical Association’s Advisory Committee to the Energy Information Administration (EIA).
Prior to joining The Brattle Group, Mr. Hanser held teaching positions at the University of the Pacific, University of California at Davis, and Columbia University, and served as a guest lecturer at the Massachusetts Institute of Technology, Stanford University, and the University of Chicago. He is currently a Senior Associate, Mossavar-Rahmani Center for Business and Government, Harvard Kennedy School. He has also served as the manager of the Demand-Side Management Program at the Electric Power Research Institute (EPRI). He has been published widely in leading industry and economic journals.
Insert corporate headshot here.

## Slide 26: Speaker Bio and Contact Information
The views expressed in this presentation are strictly those of the presenter(s) and do not necessarily state or reflect the views of The Brattle Group, Inc.
Speaker Bio and Contact Information
Sanem Sergici
Senior Associate
Cambridge, MA
Sanem.Sergici@brattle.com
Phone: (617) 864-7900
Fax: (617) 864-1576
Dr. Sanem Sergici is a Senior Associate in The Brattle Group’s Cambridge, MA office with expertise in electricity markets, applied econometrics, and industrial organization. At Brattle, the focus of Dr. Sergici’s work has been on assisting electric utilities, regulators, and wholesale market operators in their strategic questions related to energy efficiency, demand response, and customer behavior in the context of Smart Grid. Dr. Sergici has significant expertise in the design and evaluation of dynamic pricing pilot programs; development of load forecasting models; ratemaking for electric utilities; and energy litigation. Her most recent engagements include assisting the utilities in Michigan, Connecticut, Illinois and Maryland in the design and impact evaluation of their pricing and technology pilots. She has spoken at several industry conferences and published in several industry journals.
Dr. Sergici received her Ph.D. in Applied Economics from Northeastern University in the fields of applied econometrics and industrial organization. Her Ph.D. dissertation investigated three important aspects of U.S. electricity restructuring, namely divestures of generation, ISO/RTO formation, and the utility merger wave. She received her M.A. in Economics from Northeastern University, and B.S. in Economics from Middle East Technical University (METU), Ankara, Turkey.
Insert corporate headshot here.

## Slide 27: Firm Overview
The Brattle Group provides consulting and expert testimony in economics, finance, and regulation to corporations, law firms, and governments around the world.
We combine in-depth industry experience and rigorous analyses to help clients answer complex economic and financial questions in litigation and regulation, develop strategies for changing markets, and make critical business decisions.

## Slide 28: Areas of Expertise
  Functional Practice Areas
  Antitrust/Competition
  Commercial Damages
  Environmental Litigation and Regulation
  Forensic Economics
  Intellectual Property
  International Arbitration
  International Trade
  Product Liability
  Regulatory Finance and Accounting
  Risk Management
  Securities
  Tax
  Utility Regulatory Policy and Ratemaking
  Valuation
  Industry Practice Areas
  Electric Power
  Financial Institutions
  Natural Gas
  Petroleum
  Pharmaceuticals, Medical Devices, and Biotechnology
  Telecommunications and Media
  Transportation

## Slide 29: Our Experts
Our project teams are led by economists and consultants who share a strong commitment to their profession, clients, and colleagues.
Our principals hold advanced degrees from top universities around the world and have earned reputations as experts in their fields from their work in public and private corporations, academia, and government positions.
We maintain ties to internationally renowned academics and former government officials, and they bring academic and research expertise and industry credentials to our client teams.
Our associates possess exceptional analytic, project management, and research skills. They hold graduate degrees and have strong industry experience.
Principals
Senior Advisors
Associates

## Slide 30: Contact Us
North America
Cambridge, MA
+1.617.864.7900
San Francisco, CA
+1.415.217.1000
Washington, DC
+1.202.955.5050
Europe
Brussels, Belgium
+32.2.234.77.05
London, England
+44.20.7406.7900
Madrid, Spain
+34.91.418.69.70
www.brattle.com