Chapter 4: Background Information and Joint Fact Finding Road-Map (or could be Appendix X?) [Note: Links are not live but will be added in final report—put all documents in one place w/clearing name/date in report.  AG to propose redlines for pilot section.  ]

#### A) Grid-Facing

The Grid-Facing Committee asked the utilities two sets of questions regarding the status of the existing grid-facing infrastructure.  The purpose of these questions was to provide a general overview of the current grid-facing infrastructure, and perhaps an indication as the extent to which the utilities have adopted grid modernization capabilities and network system enablers (see Figure 3.1).

The first set of questions was intended to get descriptions; installation dates; the levels of deployment of various technologies; and additional characteristics of the various network system enablers.  The second set of questions was focused on the utilities’ current capabilities for integrating distributed generation onto their systems; including information regarding the measurement/estimation of minimum load, equipment to readily integrate distributed generation resources, and additional relevant data.  The questions asked, and the utilities responses to them are available HERE.

The responses to the first set of questions are summarized below in Tables 4A1, A2, and A3.  Table 4A1 provides an overview of the substations, feeders and capacitors that are currently installed on the utility systems.  For each utility, and for each technology type, the table presents the total number, the number of automated technologies, and the percent of the total that is automated.  This table also provides some definitions of the different technology categories.

Table 4A2 provides more details, including the types of network system capabilities (e.g., fault detection, integrated volt/VAR control, remote monitoring) that are located on each utility system.  This includes information on the level of the system at which the capabilities are located, including transmission system level, distribution system level, substation level or neither.

Table 4A3 provides additional details for the network system enablers.  This includes when they were installed, status of recent upgrades, and future plans for upgrades.

Note: The utility responses to the second set of grid-facing questions (pertaining to capabilities with regard to installation of distributed generation) were not provided in time to include in this draft of the report (but can be added on subsequent drafts).Flesh this out in description, and consider what tables should be included

Table 4A1

|  | Substations1 | Feeders2 | Capacitors3 |
| --- | --- | --- | --- |
|  | Total | Automated | Percentage | Total | Automated | Percentage | Total | SCADA Control | Percentage | Automated Response | Percentage |
| NSTAR | 200 | 120 | 60% | 1579 | 995 | 63% | 830 | 640 | 77% | 95 | 11% |
| WMECo | 28 | 10 | 36% | 233 | 134 | 58% | 250 | 62 | 25% | 77 | 31% |
| National Grid | 258 | 138 | 53% | 1028 | 567 | 55% | 2500 | 0 | 0% | 1800 | 72% |
| Unitil | 11 | 4 | 36% | 36 | 14 | 39% | 135 | 0 | 0% | 40 | 30% |

| Category Definitions | 1 Substation automation is defined as the full SCADA integration (status, control and analog data) of the substation for all major equipment (power transformers, substation capacitors and breakers/reclosers). This may or may not include the power transformer LTC and/or individual phase regulators for distribution feeders. In some cases partially automated substations (portion of a substation is fully automated without all distribution feeders being fully automated) have been included in the count (a very small percentage of feeders are in this category). "Full" automation does not typically include feeder phase regulators but does include LTC automation for new installations. | 2 Feeder automation is defined as the full SCADA integration (status, control and analog data) of the feeder breaker/recloser within the substation fence and/or the SCADA control of automatic sectionalizing devices outside the substation fence on the distribution feeder. Additionally non- communication enabled automated loop sectionalizing schemes and/or preferred/alternate schemes have been included as well as more advanced multi-switch/multi-feeder communicating FDIR schemes. These figures include both overhead and underground feeders | 3 Capacitor counts included in this table are line banks only, not substation banks. SCADA control is defined as the ability to send a signal to remotely operate the bank and may or may not include status of the bank. Automated response is defined as the presence of a local control capable of operating the bank programmatically based on time, day, date, temperature and/or power quantity values (voltage, current, KW flow, KVAR flow, etc.). |
| --- | --- | --- | --- |

Table 4A2

| NSTAR |
| --- |
| System Location Notes |
| Fault Detection, Isolation, Restoration (FDIR) | Distribution system and substations | 80 auto reconfiguration loops, with 100 additional planned for 2013 |
| Automated Feeder Reconfiguration | Distribution system and substations | FDIR devices continuously monitor system, alerting operators of loading concerns. |
| Integrated Volt/VAR Control, Conservation Voltage Reduction | Transmission, distribution, substations | 830 Capacitor bank, of which 640 are controllable remotely. No CVR. |
| Remote Monitoring & Diagnostics ( equipment conditions) | Transmission, distribution, substations | All major equipment is remotely monitored via SCADA i.e. Substation transformers, remote controlled switches, communications, etc.. |
| Remote Monitoring & Diagnostics (system conditions) | Transmission, distribution, substations | All remote controlled reclosers and ASUs monitor the system providing voltage, current and power factor. |

| WMECo |
| --- |
| System Location Notes |
| Fault Detection, Isolation, Restoration (FDIR) | Distribution system | 120 recloser loop schemes on its system. All loop schemes operate automatically in response to loss of source voltage. |
| Automated Feeder Reconfiguration | None |  |
| Integrated Volt/VAR Control, Conservation Voltage Reduction | Distribution system and substations | Manage voltage within a +/- 5% bandwidth, no CVR |
| Remote Monitoring & Diagnostics ( equipment conditions) | Substation | Alarms alert operators for various abnormal conditions. No capability to remotely sense specific equipment conditions (e.g. oil levels) or diagnose problems. |
| Remote Monitoring & Diagnostics (system conditions) | Distribution system and substations | DSCADA for remote monitoring and diagnostics of system conditions. |

| Unitil |
| --- |
| System Location Notes |
| Fault Detection, Isolation, Restoration (FDIR) | Distribution system | One circuit currently has FDIR recloser combination |
| Automated Feeder Reconfiguration | None |  |
| Integrated Volt/VAR Control, Conservation Voltage Reduction | Distribution system and substations | Manage localized circuit level power factor and voltage through the use of capacitor banks that are automatically controlled based on system condition or time of day. |
| Remote Monitoring & Diagnostics ( equipment conditions) | None |  |
| Remote Monitoring & Diagnostics (system conditions) | Distribution system and substations | SCADA is installed in 4 of 11 substations. This includes remote monitoring on 4 capacitor banks, approximately 45 breakers/reclosers, and 6 transformers. |

| National Grid |
| --- |
| System Location Notes |
| Fault Detection, Isolation, Restoration (FDIR) | Distribution system | Approximately XX non-communicating or communicating loop sectionalizing schemes and/or preferred/alternative schemes Small rollout of Advanced Distribution Automation (multi-switch/multi- feeder communicating system) as part of SG pilot |
| Automated Feeder Reconfiguration | None |  |
| Integrated Volt/VAR Control, Conservation Voltage Reduction | Distribution system | Advanced Local Volt/Var Control: Small rollout as part of SG pilot 2.5/5% voltage reduction on 75% of feeders per NE-ISO operating procedures |
| Remote Monitoring & Diagnostics ( equipment conditions) | Transmission, distribution, substations | A small subset of large power transformers have remote condition monitoring via SCADA, additionally SCADA alarms alert operators of various abnormal conditions on a wider range of distribution and transmission equipment. A small rollout of devices as part of the SG pilot will provide equipment monitoring on all new devices. |
| Remote Monitoring & Diagnostics (system conditions) | Transmission, distribution, substations | SCADA for remote monitoring and diagnostics of system conditions within the substation fence. Also remote controlled reclosers monitor the system providing voltage, current and power factor. A small rollout of new equipment as part of the SG pilot will provide near real time monitoring of system conditions at several locations on the pilot feeders. |

Table 4A3

Type                                                                                                       When Installed                                Most Recent Upgrade         Future Plans                                                                                                                             Notes

NSTAR

Distribution Management System (DMS)/SCADA

GE SCADA/EMS:  Trans, Sub-trans, North Distribution              1994                                                   2007                                         Migrate and implement auto-restoration schemes                                                        1,100+ supervisory, and 60,000+ analog & digital points

GE Powerlink Advantage: South Distribution                               2005                                                   2011                                                                                                                                                                                              750+ supervisory, and 40,000 analog & digital points.

Outage Management System (OMS)                                                                                                                                                                                                                                                                                                                                                                                                                                                      CGI PragmaLine v2.03                                                                        2000                                                   Replaced

GATOR                                                                                                   2003                                                                                                     Planned replacement 2013-2014

Geospatial Information System (GIS)                                                                                                                                                                                                                                                                                                                                                                                                                                                     Editor: Custom ESRI                                                                            North: 1990s, South: 2004            Upgrade in progress

Viewer: ESRI ArcMap with customization                                     2004                                                   Upgrade in progress

Transmission Editor: ArcFM                                                             2008                                                   Upgrade in progress

GIS-OMS Integration                                                                                                                                                                                                                                                                                                                                                                                                                                                                                  GATOR-GUI                                                                                           2003 (within OMS upgrade)         GIS upgrade in progress      OMS Replacement 2013-2014

Billing System

1991                                                   Continuous

Metering System                                                                                                                                                                                                                                                                                                                                                                                                                                                                                         Premierplus4                                                                                        ?                                                          Replaced

FCS (Field Collection System)                                                           2012                                                   Underway

Route Smart ArcGIS                                                                            2007                                                   2011

MV90 (Interval Meter Collection)                                                   2006                                                   2009                                         Upgrade in 2013                                                                                                                      for 7000 TOU meters via modem and cellular networks

Meter Data Management System (MDM)                                                                                                                                                                                                                                                                                                                                                                                                                                            Lodestar                                                                                                2011

OMS-AMR/AMI Integration                                                                                                                                                                                                                                                                                                                                                                                                                                                                      N/A                                                     N/A

Communication Systems                                                                                                                                                                                                                                                                                                                                                                                                                                                                           Various systems                                                                                  2008-2010

Type                                                                                                       When Installed                                Upgrades                                Future Plans                                                                                                                             Notes

WMECO

Distribution Management System (DMS)/SCADA

Siemens Spectrum Power TG                                                           2002                                                   currently upgrading                                                                                                                                                                  2400+ devices, 280,000+ analog & digital points.

Outage Management System (OMS)                                                                                                                                                                                                                                                                                                                                                                                                                                                      Oracle Network Management System                                           2004                                                   2007                                         upgrade/replacement  in 2014

Geospatial Information System (GIS)                                                                                                                                                                                                                                                                                                                                                                                                                                                     Editor:  GE Smallworld Editor                                                           2002                                                   2008

Viewer:  GE SIAS Viewer                                                                    2010

Transmission Editor                                                                            N/A                                                     N/A                                           Integration into Smallworld editor around 2013

Viewer:  ESRI SilverLight Viewer - custom                                     2012

GIS-OMS Integration                                                                                                                                                                                                                                                                                                                                                                                                                                                                                  Smallworld                                                                                            2004                                                   2008                                         replacement in 2014

Billing System                                                                                                                                                                                                                                                                                                                                                                                                                                                                                               C2 Application                                                                                      2008                                                   Continuous

Metering System                                                                                                                                                                                                                                                                                                                                                                                                                                                                                         Fieldnet                                                                                                 1990s                                                 2012                                         Upgrade in 2014

Prime Read (Interval Meter Collection)                                         2008                                                                                                     Move all to MV90 and retire application

ION Revenue                                                                                        2005                                                                                                     Move all to MV90 and retire application

Meter Data Management System (MDM)                                                                                                                                                                                                                                                                                                                                                                                                                                            Lodestar MDM                                                                                     2013

SerViewCom                                                                                         ?                                                          2010                                         Move all to MV90 and retire application

EVEE Meter Data Warehouse                                                           2003                                                   2012

OMS-AMR/AMI Integration                                                                                                                                                                                                                                                                                                                                                                                                                                                                      N/A                                                     N/A

Communication Systems                                                                                                                                                                                                                                                                                                                                                                                                                                                                           Fiber                                                                                                       2005-2013

Microwave                                                                                            2005-2013                                                                                           Some will be replaced by fiber, where appropriate

Mobile Radio                                                                                        2005-2008

DSCADA Radios                                                                                    2012-2013

Type                                                                                                       When Installed                                Upgrades                                Future Plans                                                                                                                             Notes

National Grid

Distribution Management System (DMS)/SCADA

None                                                                                                      N/A                                                     N/A                                           Planned OMS and EMS SCADA interface after OMS installation in fall 2013 to support potential future DMS

Outage Management System (OMS)                                                                                                                                                                                                                                                                                                                                                                                                                                                      PowerOn                                                                                               2006                                                                                                     PowerOn to be replaced with ABB OMS as part of EMS upgrade during fall of 2013

Geospatial Information System (GIS)                                                                                                                                                                                                                                                                                                                                                                                                                                                     GE Smallworld                                                                                      2004                                                   2011                                         Currently using latest version (V4.2), no upgrade plans for a least three years.  T Current GIS is integrated with OMS and WMS

GIS-OMS Integration                                                                                                                                                                                                                                                                                                                                                                                                                                                                                  Fully Integrated - GE Smallworld/PowerOn                                   2006                                                                                                     PowerOn to be replaced with ABB OMS as part of EMS upgrade during fall of 2013

Billing System                                                                                                                                                                                                                                                                                                                                                                                                                                                                                               Customer Service System (CSS)                                                       2008                                                                                                     Integration of SG Pilot meter data

Metering System

Solid State (22%)                                                                                 around 2000                                     2012                                         none planned, but Smart Grid Pilot underway                                                                .297 million meters.  92% of all National Grid meters read via Drive-by AMR

#### B) Time-Varying Rates

Time varying rates (TVR aka dynamic pricing) issues and experience in the U.S. and abroad were presented by the Brattle Group at the Kick-Off Summit (See Brattle Presentation HERE 11/14/12).  The Customer-Facing Subcommittee then heard detailed presentations regarding the smart grid pilots from NSTAR, NGRID, and UNITIL at its first meeting (See Utility Presentations Here 1/9/13), and the Steering Committee heard an updated presentation on NSTAR’s pilot at its 5th or 6th meeting (See NSTAR Presentations HERE 5/?/13).  At the second Customer-Facing Subcommittee meeting, the Regulatory Assistance Project presented additional information on experience and issues in the U.S. and abroad on TVR, and the Attorney General’s consultant presented both the principles developed by NASUCA et al on consumer protections related to TVR and AMI as well as additional recent experience across the U.S. on TVR and AMI (See RAP and NASUCA presentations HERE 2/26/13).  Finally, at the 5th Steering Committee the Attorney General presented some research it had done on TVR in other restructured states (See Basic Service Memo & AG TVR Table HERE 5/14/13).  The following tables and graphs extract some of the summary tables and highlights from these presentations; however, please see the actual presentations and the meeting summaries from the meetings in which the documents were presented and discussed for the full details.

Current rates for basic service customers of Massachusetts investor-owned utilities are essentially a flat rate that does not vary by time of day, day of the week, or by season. Time varying rates are rates that have some variability based on when energy is consumed.  As Table B1-X illustrates there is a continuum of ways to design rates to make them more or less reflective of the changes in price at the wholesale level.  These range from time-of-use (TOU) rates that divide the day into two or three time periods with different rates that are then fixed for a season or a year, up to real-time pricing (RTP) where prices can change hourly to reflect wholesale pricing conditions.  Critical peak pricing (CPP is generally an overlay on TOU pricing that allows for prices to rise significantly at pre-announced times when costs are projected to rise significantly.  Peak time rebates (PTR) is an alternative TVR approach where customers are given a rebate for reducing load generally during critical peak periods.

Table 4-B1: Rate Continuum: Static to Dynamic

Figure 4-B1 shows a depiction of the range of TVR options and how the potential reward (discount from flat rate) compares to the risk (variance in price).  The chart shows that real-time pricing (RTP potentially has the highest reward for customers but also has the highest risk.  Time-of-using pricing (TOU) on the other hand has a much lower potential reward but also a much lower risk—with CPP falling between the two.  Peak-time-rebates (PT) by contrast, provide a reward (in the form of a rebate) but no real risk (since you only get a rebate when you reduce, but are not penalized if you do nothing).

Figure 4-B1: Risk-Reward Tradeoff in Time-Varying Rates

Figure 4-B2, presented by Brattle and by RAP, is a graph of the peak reduction and the peak to off-peak price reduction from 74 TVR pilot programs across the U.S.  It illustrates two points.  First, higher peak to off-peak price ratios generally elicit higher responses in the form of peak reductions than lower ratios.  Second, TVR associated with enabling technology that facilitates load management actions generally increases the peak reduction response.

Figure 4-B2: Peak Reduction Relationships to Price Ratio & Enabling Technology

The Massachusetts distribution companies are in various stages of completing their smart grid pilots (except for WMECO which doesn’t have an approved pilot), which are testing a range of TVR rates as well various metering and other enabling technologies.  It’s important to keep in mind that the pilots were all “opt-in” and are therefore a self-selected group of customers.  Unitil, which already had installed a form of AMI metering for all its customers, has completed their pilot.  Unitil used a TOU rate with and without enhanced technology and smart thermostats.  They found kw reductions with the TOU without enhanced technology of 21% on-peak and 42% during the critical peak period.  The savings with the enhanced technology added increased to 35% for on-peak and 70% during the critical peak.  The customer bill savings averaged 5% for the simple TOU and 7% with the enhanced technology.

Table 4-B2: Unitil’s Smart Grid Pilot Results

NSTAR is still in the middle of its pilot, which is scheduled to be completed at the end of 2013.  NSTAR is using its pre-existing AMR meters enhanced with home area networks for its pilot.  As Table 4-B3 describes, NSTAR is testing 3 different TVR approaches (PTR with NSTAR control of a smart thermostat, and TOU with CPP with and without enabling technology), plus a control group with only enhanced information but standard rates.  Figure 4-B3 below shows the interim peak savings during both the summer and winter for all 4 groups of participants.  The 3 TVR groups appear to have saved more kw during both the summer and winter peak periods than the enhanced information alone control group—but there doesn’t appear to be a clear winner among the two TOU options and the PTR option in terms of which performed better overall in terms of kw reduction in both the winter and summer seasons.  The final evaluation and numbers on this pilot should be available in the spring of 2014.

Table 4-B3 NSTAR’s Smart Grid Pilot Customer Test Groups

Figure 4-B3 NSTAR’s Average Peak Period Load Reductions (January-September 2012)

National Grid is just in the process of rolling out its smart grid pilot in Worcester, so no data is available yet except their approved design and initial experience with meter installation.  Although NGRID already has AMR meters, it is planning on installing 15,000 AMI meters for the pilot participants.  It will offer three different TVR options to its customers: 1) CPP for residential and small C&I; 2) PTR option also for residential and small C&I; and 3) HPP—hourly pricing for largest C&I customers.  It will allow customers to opt out of meter installation and CPP or HPP.  As Figure 4-B4 shows there will also be various combinations of technology options (home display units, smart thermostats and automatic HVAC controls, and load control devices.)  Meter completion was scheduled form May 31, 2014 and the pilot TVR pricing starts January 1, 2014.

Figure 4-B4: National Grid’s Smart Grid Pilot

As Figure 4-B5 describes, the Massachusetts utilities currently has mandatory TOU distribution (portion) rates for its largest C&I customers.  However, for residential and small C&I customers there are legacy optional TOU rates that have been in place for some time but are neither aggressively marketed by the utilities nor well-subscribed by customers.

Figure 4-B5: Legacy Massachusetts Utilities TOU Rates

Table 4-B4 is a summary of research done by the Attorney General’s Office on the use of TVR by other restructured states.  It found that in each of the states basic service is a flat rate, with a range of TOU and PTR rates that are available on a voluntary opt-in basis.

Table 4-B4: TVR and Metering in Other Restructured States

| State/Utility | Type of Metering Prior To AMI (Manual Read, AMR) | Type of Metering (AMI, AMR, or Enhanced AMR) | Basic Service Design | Type of TVR (TOU, TOU/CPP, or PTR) | On Basic/Default Service (supply) Distribution Rates, or Both | Opt-In, Opt-Out, or Mandatory |
| --- | --- | --- | --- | --- | --- | --- |
| Connecticut |  | Not AMI | Flat Rate | Legacy TOU | Supply Only | Opt in |
| Delaware | Manual Read | AMI | Flat Rate | TOU legacy and PTR | Both | Large scale PTR pilot underway; participation is opt in |
| District of Columbia* | Manual Read | AMI | Flat Rate | TOU legacy | Supply Only | Opt in |
| Illinois | Various | AMI (over 10 years) | Flat Rate | "Real Time" Pricing since 2009; Legacy TOU; PTR in future | Supply Only | Opt in |
| Maine* | Manual Read | AMI - CMP | Flat Rate | TOU | Supply Only | Opt in |
| Maryland* | Manual Read | AMI being installed | Flat Rate | Legacy TOU and PTR | Both | Overlay on Basic; participation is opt in |
| Michigan* | Manual Read | AMI (over 10 years) | Flat Rate | TOU | Supply Only | Opt in |
| New Hampshire |  | Not AMI | Flat Rate | TOU legacy | Distribution Only | Opt in |
| New Jersey |  | Not AMI | Flat Rate | TOU legacy | Both | Opt in |
| New York |  | Various; not AMI | Flat Rate | TOU legacy | Both | Opt in |
| Ohio* | Various | AMI only for Duke and AEP | Flat Rate | TOU legacy; pilot TOU for AMI | Supply Only | Opt in |
| Pennsylvania* | Various | AMI (over 10 years) | Flat Rate | TOU with installed AMI; PTR for one utility | Supply Only | Opt In |
| Rhode Island |  | Not AMI | Flat Rate | None | NA | NA |
| Texas* | Various | AMI | None | Unknown | Unknown | Opt in |
| Notes: |
| 1. This information reflects residential rates only. |
| 2. Several of these utilities offer optional EV charging TOU rate with or without AMI |
| 3. In these states, licensed suppliers can offer TVR but these rate options are not typical of nost offers |
| * means that one or more utilities in these states received ARRA funding for up to half of the AMI deployment costs 4. Original spreadsheet also includes description of any TVR or PTR, and whether administered by utility or another (see original on the website at Steering Committee Meeting # 5) |
| Source: Office of the Attorney General |

- Baseline information (summarize response to data requests) (Tim—anything else important on TVR not included above?)

#### C) Metering

Metering issues and discussion permeated numerous Steering Committee meetings as well as both Customer-Facing and Grid-Facing Subcommittee meetings.  There were three different pieces of meter-related work overseen primarily by the Customer-Facing Subcommittee to help the Members garner a better understanding of the current metering infrastructure in Massachusetts and opportunities.  First, through two sets of data requests the utilities provided information on their current metering infrastructure and replacement protocols (See first set of NU, NGRID, & Unitil Metering Questions HERE 2/26/13 as well as Compilation of Metering Responses HERE 4/4/13 and See second set of utility metering responses and update compilation HERE probably for 5/22 TBD).  The second thing was to have presentations by three meter-related hardware and software vendors—focusing on options for enhancing metering infrastructure including types of technology, functionality, and cost (See presentations by Itron, AvCom, and Sentinel Works HERE 1/9/13).  Lastly, the Customer-Facing Subcommittee and a metering working group that they formed to assist them spent a substantial amount of time fleshing out various metering technology options and then how those technologies could support a range of customer-facing and grid-facing capabilities and functions—identifying the incremental functionality of various technologies.  The work group and Subcommittee also attempted to develop cost ranges for the various technologies including the meter cost, installation, and a range of necessary supporting infrastructure. The cost data was initially supplied from ITRON studies, and then massaged by the utilities based on their own systems and experience from the pilots to date (See Metering Technologies Functions Costs spreadsheet with the various worksheets HERE 4/23—note jdr needs to update first w/clean energy worksheet).

The Massachusetts investor-owned utilities, with the exception of Unitil, all converted their meters from manual-read meters to AMR meters during the 1990’s through the last decade.  The AMR meters read from a moving vehicle rather than a meter reader.  Unitil converted its meters to a form of AMI around 10 years ago, which allows Unitil to access the metered data remotely without having to drive by or manually read the meter.  Table 4-C1 shows the approximate age of the current meters for each utility as well as each utility’s assumed book life and operating life.  Based on the information provided by the utilities, the consultants calculated the last line in the table which shows the average life remaining in the existing meters.

Table 4-C1: Utility Metering Infrastructure—Age, Book Life & Operating Life

|  | NSTAR | WMECO | National Grid | FG&E |
| --- | --- | --- | --- | --- |
| Approximate average meter age (years) | Energy 10 | Energy 12 |  |  |
|  | Demand 7 | Demand 8-9 | 17.8 | 7.1 |
|  | TOU 5 | TOU 2 |  |  |
| Book life (years) | 24 | 23 | 28.9 | 20 |
| Operating life (years) | 15 - 20 | 15 - 20 | 30 | 20 - 30 |
| Approx. avg. life remaining (years) | 5-15 | 3-18 | 12.2 | 12.9 - 22.9 |

Figure 4-C1 shows a schedule of when the current meters were installed on each utility’s system.  The figure shows the percent of the total meters that were installed in each year.  For example, of all the meters currently installed on the Unitil system, roughly 70 percent were installed in 2006.  As another example, for National Grid roughly 30 percent of the current meters were installed in 2002.  Current practice is to replace failed or aged meters with “like” meters (e.g., AMR with AMR).  This information was provided by the utilities in response to a request for information from the Customer-Facing Subcommittee.  The questions and responses can be found HERE.

Figure 4-C1: Schedule of Current Meter Installment: Percent of Total Installed in Year

The Customer-Facing Subcommittee with the help of a work group that it created, first developed a range of metering technology options beginning with AMR, which is currently the most common meter type in Massachusetts, up through advanced metering infrastructure.  It included several options to enhance basic AMR meters either through home area networks or fixed external area networks—both able to provide information back at the home office without having to drive by.  The work group and Subcommittee also heard about a new ITRON metering technology called a “Bridge AMI Meter” which can continue to act as an AMR meter, and the be switched remotely into AMI mode once the utility has all other supporting AMI infrastructure in place.  Finally the work group and Subcommittee looked at Unitil’s AMI system—which is a more limited AMI than full AMI, and looked at basic AMR with load control.

Table 4-C2: Metering Technology Options

The next thing that was done was to identify the potential meter-related functionality of interest both on the customer-facing side and the grid-facing side—identifying a total of 11 areas of focus shown in Table 4-C3. The work group and ultimately the Subcommittee than populated a matrix comparing each of the technologies in a different row, with each of the 11 potential functions in a separate column to see what each technology was capable of providing.  To see the detailed matrix, please see the worksheet labeled “Functionality” on the website (HERE 4/23—note jdr needs to update first w/clean energy worksheet), A summary of the incremental customer-facing and grid-facing functionality for key metering technology options is shown below in Table 4-C4: Incremental Functionality of Metering Options.  It shows that as you move from AMR, through two types of enhanced AMR to AMI, additional functions “can” be supported by the meters and associated infrastructure.

The work group and Subcommittee also worked on the costs related to the different metering technology options—including the meter and installation, a range of supporting infrastructure costs, and O&M costs.  The costs were put in ranges and developed with the assistance of Itron (the largest meter manufacturer in the world) and the utilities experiences with their own infrastructure and pilot programs.  (See Table 4-C5: Metering Technologies and Costs below).  A final exercise that the Subcommittee did was look at the meter-related customer-facing and grid-facing functionality compared to various clean energy related activities of interest (demand response, distributed generation, direct load control, electric vehicles, etc.).  Looking across the wide range of clean energy related activities the metering related functionality of greatest relevance appears to be 1) communication to the meter and from the meter to customer devices; and 2) access to interval data on a real time basis.  However, for some activities, such as electric vehicle recharging, if a time of use rate is sufficient, access to a TOU register instead of interval data on a real time basis might suffice.  (See Functionality & Applications worksheet of Metering Technologies Functions Costs spreadsheet HERE 4/23 JDR needs to update and accompanying text Metering Functionality & Clean Energy Activity Text HERE 4/23)  The Subcommittee communicated to the Steering Committee that just because a certain type of meter “can” support a particular capability or function, doesn’t mean that it is necessarily the only way to enable those functions (e.g., direct load control can be accomplished without going through the meter) or that it is necessarily cost-effective.  However, measurement and verification without interval data becomes more complicated particularly if end use being contoled is not homogenous or if the customers is allowed to opt out.

The Subcommittee and Steering Committee did not endeavor to do a cost-effectiveness analysis of the different metering technologies and their associated incremental functionality benefits.  Rather it is assumed that this will need to be done on a company by company basis at the appropriate time.

Table 4-C3: Meter-Related Functionality

Table 4-C4: Incremental Functionality of Metering Options

| Technology Options: | Customer-Facing | Grid-Facing |
| --- | --- | --- |
| AMR | Drive-By Meter Reading; One-Way Communication |  |
| Enhanced AMR (w/HAN) | AMR PLUS Communication to Customer Equipment and MAY enable Remote Meter Read, TOU Register, Daily & Real-Time Meter Read | MAY enable Outage ID & Restoration Notification |
| Enhanced AMR (w/Fixed Network) | AMR PLUS Remote Meter Read, TOU Register, Interval Data, Daily Read, and MAY also enable Real Time Data Read, Communication to Customer Equipment | MAY/limited Outage ID & Restoration Notification, and Planning Data |
| Full AMI | AMR (w/Fixed Network) PLUS Real Time Data Read, Two-Way Communication to Meter, Communication to Customer Equipment, | AMR (w/Fixed Network) PLUS Remote Service Connect/Disconnect Switch, Voltage Reading, Power Quality Reading |

Note: “MAY” is due to fact that some of functionality may not be available depending on model buy or may need to purchase the additional functionality

Table 4-C5: Meter Technologies and Costs

|  | Meter (equipment) Costs | Installation Costs | Home Area Network Enablement | Software & Network Infrastructure | Other Smart Grid Infrastructure (OMS, DMS, GIS) | Total Cost (1) | DLC at Device (for interested customers) | Annual O&M (as percent of capital cost) |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| I) AMR Only (NU/NGRID SQ) | $30-50 | $20-40 | NA | $2 | NA | $52-92 | $100-150 | 10-30% |
| A) Swap Individual Meters for TOU--Drive By | $120 | $20-40 | NA | $2 | NA | $142-162 | $100-150 | 10-30% |
| 2) Enhanced AMR |  |  |  |  |  |  |  |  |
| A) Home Area Network/Software | $30-50 | $100-200 | $125-175 | $2 | NA | $257-422 | $100-150 | 10-30% |
| B) Fixed Area Network/Software | $30-50 | $20-40 | NA | $15-30 | NA | $65-120 | $100-150 | 10-30% |
| C) Swap Individual Meters for TOU—Wireless | $300-600 (C&I only) | $20-40 | NA | $2 | NA | NA | $100-150 | 10-30% |
| 3) Bridge AMI (new ITRON meter) |  |  |  |  |  |  |  |  |
| A) AMR (mobile) Mode | $120 | $20-40 | $125-175 | $ 2 | NA | $167-207 | $100-150 | 10-30% |
| B) AMI (network) Mode | $120 | $20-40 | $125-175 | $50-125 | $50-190 | $265-500 | $100-150 | 10-30% |
| 4) AMI (Unitil SQ) | $70-150 | $20-40 | $75-150 | $50-125 | $50-190 | $265-655 | $100-150 | 10-30% |
| 5) Full AMI (2) | $80-150 | $20-40 | $125-175 | $50-125 | $50-190 | $325-680 | $100-150 | 10-30% |
| 6) AMR & Direct Load Control |  |  |  | $5-10 |  |  | $100-150 | 10-30% |

Notes:

(1) The Total Costs are simply a total of the min-max individual costs. Actual upgrade costs will vary based on functionality deployed.

(2) Ranges on AMI in part related to different functionality

(3) Cost estimates based on combination of ITRON supplied cost, and MA utility experience

(4) In 3B if Bridge Meter already installed in "mobile" mode, no incremental equipment or labor cost to switch to AMI (network) mode

(5) Row 2A is based on NSTAR pilot costs, scale deployment could be different

(6) Software/Network Infrastructure cost relatively fixed, and likely lower cost/meter for large systems than small

(7) Other Smart Grid Infrastructure can vary significantly depending on pre-existing infrastructure and what other options to pursue

and based on ITRON's analysis of other jurisdictions

(8) For DLC end costs/installation same, but communications cost vary significantly--i.e., likely less expensive for AMI

# Footnotes

According to NGRID of the first 5,000 meters installed, 297 or 6% of customers opted to not have meters installed.