## Slide 1: Unitil Smart Grid Pilot Pilot Design and Results
Electric Grid Modernization Working Group Customer Facing Subcommittee
January 9, 2013

## Slide 2: Unitil Smart Grid Pilot
Utility Goals and Objectives
Pilot Overview
Results & Observations
1

## Slide 3: Goals and Objectives
Meet Regulatory Requirements:
  MA Green Communities Act, signed July 2008
  NH’s instigation of Energy Policy Act of 2005, concluded in 2008, encouraged Unitil to initiate a TOU Pilot Program.
Future DR program decisions: Obtain results on impacts, costs, and customer satisfaction
Test capabilities of current AMI metering environment
Investigate IT projects: Test and gain experience with MDM system, billing integration, and online web portal
Maintain high customer satisfaction!
2

## Slide 4
Residential Pilot Structure
“Energy Savings Management”
Simple TOU
76 Customers
Time of Use pricing
No technology
Enhanced TOU
76 Customers
Time of Use pricing
In-home Energy Management System
Smart Thermostat
76 Customers
NO Time of Use pricing
Direct A/C Load Control
Control Group
76 Customers
Flat rate pricing
No technology
3

## Slide 5
Distribution of Customers by State
Sample Group | Mass | NH
Time of Use | 24 | 52
Enhanced Technology | 24 | 52
Smart Thermostat | 24 | 52
Control Group | 24 | 52
Commercial TOU |  | 30
Totals: | 96 | 238
4

## Slide 6: Project Schedule
April 6th, 2011 Initiate in-home installations
April 20th, 2011 Enrolled 2nd batch of customers
May 6th, 2011 Customer web portal active
May 13, 2011 Billing System Tested
May 18, 2011 In-home installations complete
June 1, 2011 Pilot Begins
August 31, 2011 Pilot Ends
October 2011 Evaluation and Reporting
Dec. ‘11 - Jan ‘12 Filed Report with DPU & NHPUC
5

## Slide 7
6
Weekday Time of Use Rate (Non-CPP)
off
-
peak period
4.748¢ / kWh
off
-
peak period
4.748¢ / kWh
on
-
peak period
10.846¢ / kWh
$0.00
$0.02
$0.04
$0.06
$0.08
$0.10
$0.12
$0.14
12:00 AM
6:00 AM
12:00 PM
6:00 PM
11:00 PM
Weekday TOU Rate (Non
- CPP)
“On-Peak”
12pm-6pm Weekdays.
“Off-Peak”
Mornings, Nights, Weekends & Holidays.
6
Notes: 6

## Slide 8
7
Critical Peak Weekday TOU Rate
5 Critical Peak Periods declared during the 3 month pilot period
Customers notified by 5pm day prior by phone & email
off
-
peak period
4.748¢/ kWh
off
-
peak period
4.748¢/ kWh
Critical
-
peak period
64.642¢/ kWh
$0.00
$0.10
$0.20
$0.30
$0.40
$0.50
$0.60
$0.70
12:00 AM
6:00 AM
12:00 PM
6:00 PM
11:00 PM
Critical Peak Weekday TOU Rate
Notes: 7

## Slide 9
8
Simple TOU Group
Low cost DR option using existing metering technology
Customers placed on time of use rate plan (On-Peak, Off-Peak, Critical Peak)
No In-Home Technology
Customers receive access to web portal showing prior day usage & cost
8
Notes: 8

## Slide 10
9

## Slide 11: Unitil Web Portal – Usage Presentation
10
Notes: JCE – 3 or 4 minutes
History discussion
Existing AMI with TOU capability
Previously completed review of DR opportunities; targeted TOU as most cost effective approach
Regulatory requirements to conduct smart grid pilots; MA GCA (5% reduction target in demand and energy, TOU or hourly pricing);
Utility Goals
-Test capabilities of AMI system
-Evaluate cost effectiveness of different DR approaches
-New projects (MDM-p, web portal)
-Evaluate price elasticity – customer response to different price points (why we wanted multiple price points)
Pilot Design MJS add rates to notes
Residential customers with central AC
Pricing was determined based on actual LMP pricing from prior year for on and CPP periods; TOU rates were designed to be revenue neutral for an average residential customer
First group is low-cost / no-cost approach. Information only. Easily rolled out to customers
Enhanced technology group that tested incremental impact of adding home area network to TOU/CPP pricing
Third group is utility controlled, flat rate

## Slide 12: Unitil Web Portal – Cost Presentation
11
Notes: JCE – 3 or 4 minutes
History discussion
Existing AMI with TOU capability
Previously completed review of DR opportunities; targeted TOU as most cost effective approach
Regulatory requirements to conduct smart grid pilots; MA GCA (5% reduction target in demand and energy, TOU or hourly pricing);
Utility Goals
-Test capabilities of AMI system
-Evaluate cost effectiveness of different DR approaches
-New projects (MDM-p, web portal)
-Evaluate price elasticity – customer response to different price points (why we wanted multiple price points)
Pilot Design MJS add rates to notes
Residential customers with central AC
Pricing was determined based on actual LMP pricing from prior year for on and CPP periods; TOU rates were designed to be revenue neutral for an average residential customer
First group is low-cost / no-cost approach. Information only. Easily rolled out to customers
Enhanced technology group that tested incremental impact of adding home area network to TOU/CPP pricing
Third group is utility controlled, flat rate

## Slide 13
12
Enhanced Technology Group
Tendril Insight
(in-home display)
Tendril Transport (gateway)
Tendril Volt (outlet)
Tendril Mobile
Vantage Online Web Portal
Tendril Translate (ERT Bridge)
Tendril Set Point
Tested the incremental impacts of the Home Area Network (HAN)
More granular feedback on energy consumption including some appliances
The HAN can be configured to automatically control A/C and other appliances in response to price signals
12
Notes: 12

## Slide 14
13
Smart Thermostat Group
NO TOU Rate – Customers remain on current fixed rate
Customers provided with a “smart” thermostat that Unitil has the ability to control during peak events
On Critical Peak Events, Unitil cycled A/C systems 30 min on/off
Customers have the ability to “opt-out” of control events using the Yukon web portal
Customers who do not opt out of events are eligible to receive a $35 incentive at the end of the pilot
13
Notes: 13

## Slide 15: Pilot Program Results
14

## Slide 16: Additional Findings
Process Findings:
Customer Recruitment –
  Only 30% eligible due to central air
  75% turn down due to system incompatibilities
Billing – automation and integration is a requirement
Data Management – MDM needed for Web Portal
CPP Notifications – Customer information tracking
Customer Service Training
Technology Findings:
AMI:
  TOU Capabilities Confirmed
  Reliable
  Back-to-back CPP issues
HAN challenges:
  Increased turndown
  Increased failure rate
  Installation logistics
  Over the air updates
  Interval data losses
PCT paging coverage
Unitil Portal Successful but difficult to maintain
15

## Slide 17: Customer Observations
  More than 4 in 5 had a positive experience
    However, 85% of Commercial customers would not have participated without Bill Protection
  Satisfaction decreased slightly as the level of technology increased
    42% of participants with HANs experienced equipment issues
    13% of participants with PCTs only experienced equipment issues
  Many experienced problems with usability of thermostats
  Corporate structure inhibited communication for about 20% of Commercial customers
  Actions undertaken during CPP events
    Avoided use of appliances (78%)
    Pre-cooled home (56%)
    Sought activities outside the home (44%)
    Some reported aggressive actions such as shutting off main circuit breaker (impact to HANs), AC, or WH
16
Notes: JCE 1 to 2 min
Surveys were completed by roughly 40% of Unitil Pilot participants, are following up with non respondents
Smart thermostats are not always that intuitive (newer products worse than tried and true)